## Slide 1: Reinforcement Learning of a Four-Way Traffic Signal System
Joe Mockler
ENAE788Z: Decision-Making under Uncertainty
15 MAY 24

## Slide 2: Motivation and Overview
Motivation:
Interconnected traffic systems all require some form of control
Most widely adopted controller: the traffic light (~300,000 in the US)!
But how do we decide (1) what lanes to go and (2) for how much time?
Overview:
Define an MDP model of a signalized intersection
Use traditional analysis method to design a controller
Use a RL algorithm to solve the MDP and design a controller!
Notes: Don’t belabor the point, traffic lights are everywhere, but the main design question is how should we use them to decide what lanes to go and for how much time?
Overview – read through

## Slide 3: Background: Traffic Flow Theory
Terminology [7]:
Phase: part of a cycle allocated to one or more streams of traffic
Cycle: One complete sequence of the light such that every lane group gets a green
Saturation flow: flow-rate [veh/time] that a lane group can carry when the signal turns green. Note S = capacity / green time
Approach flow: incoming flow-rate for a lane group
Reproduced from [1]
Notes: We’re going to go over some basic terms to get a background
READ LANE GROUP – then switch

## Slide 4: Background: Traffic Flow Theory
Terminology [7]:
N: Left and S: Left get green
Phase: part of a cycle allocated to one or more streams of traffic
Cycle: One complete sequence of the light such that every lane group gets a green
Saturation flow: flow-rate [veh/time] that a lane group can carry when the signal turns green. Note S = capacity / green time
Approach flow: incoming flow-rate for a lane group
Reproduced from [1]
Notes: Phase: read out. It’s essentially who gets a green for what part of the cycle
Cycle: One complete sequence of the light such that every lane group gets a green
Sat flow: flow of cars immediately when the light turns green
Approach flow: incoming flow

## Slide 5: Background: Markov Decision Process Definition
Goal: Define an MDP of the signalized intersection model:(S, A, T, R,
States: (, , , ,)
Actions: (:, :)
Rewards: or -1000 if at sat.
Notes: Now let’s take a model intersection and frame it as an MDP
  Intersection have 2 lanes going NS and one EW
  The states are the queue lengths at each approach
  The actions are the phases, either Green NS or Green EW
  The reward is the negative total sum of the queue lengths
  And the transition function lets cars through when the light is green. Note that if the light switches, there’s a 2-sec all-red penalty.
ASSUMPTIONS:
No turns or complex movements
Deterministic . Stochastic that samples from a Poisson distribution.
Now let’s take a model intersection and frame it as an MDP
  Intersection have 2 lanes going NS and one EW
  The states are the queue lengths at each approach
  The actions are the phases, either Green NS or Green EW
  The reward is the negative total sum of the queue lengths
  And the transition function lets cars through when the light is green. Note that if the light switches, there’s a 2-sec all-red penalty.
ASSUMPTIONS:
No turns or complex movements
Deterministic 𝑠_𝑖. Stochastic 𝑞_𝑖 that samples from a Poisson distribution.

## Slide 6: Methods: Critical Movement and Capacity Analysis
Apply capacity analysis to MDP [7]:
Step 1, 2: Identify phases and flow-rates*
Step 3: Identify total cycle length
If then
Step 4: Allocate green times
→
*How are these estimated?
Saturation flow is usually a function of geometry
Approach flow must be estimated from forecast data or on-the-ground measurements
Notes: Let’s apply this. I have the flows the above values and prescribed the phases.
Using the formulas, the NS should get 10 sec, EW should get 8, and 2 sec is the all-red
Spend a moment on how we estimated these!

## Slide 7: Methods: Critical Movement and Capacity Analysis
Apply capacity analysis to MDP [7]:
Step 1, 2: Identify phases and flow-rates*
Step 3: Identify total cycle length
If then
Step 4: Allocate green times
→
*How are these estimated?
Saturation flow is usually a function of geometry
Approach flow must be estimated from forecast data or on-the-ground measurements
Notes: Saturation flow is a fcn of geometry – well known
But the approach flow must be estimated – either from forecasting or measurements.
  So this variable is typically uncertain! And can change throughout the day.
  In fact, most intersections perform this analysis and have dozens of cycles that change with time of day, day of week, and month to month!

## Slide 8: Methods: Maximum Likelihood
Goal: Use a model-based RL method to estimate transition and rewards to build an exploitative policy.
Notes: Now outline the RL mode
We want a RL that can overcome this limitation by learning the traffic model
Thus, use model-based max likelihood – ultimately build estimate of Q(s,a) for optimal policy under deployment

## Slide 9: Methods: Notes on Implementation
Problem: State-space will explode under current construction!
Under 4 approaches and a 50-vehicle limited queue: Q(s, a) ~ 12.5M values!
Resolution: Model reduction via grouping NS and EW lanes as a lumped queue length. With 50-veh limited queues: Q(s, a) ~ 5,000 values.
→Faster to train and easier to reason over!
Notes: Now to implement. First we must cap the number of cars in a queue to discretize the space.
  If we keep the 4-lane mode with a 50-lim cap, Q(s,a) becomes a 12.5M value dict!
  Too much to train and reason over
  Reduce to NS and EW groupings by phase instead – now only 5000!

## Slide 10: Results: Training
300 training episodes with 500 steps, each.
First 60 use heuristic to seed estimates
Next 240 use a greedy- policy with
Training plotted rollout with a=argmax[Q(s, a)] for 5 episodes after each training episode. Ribbon indicates standard deviation
Notes: 300 training episodes, 500 simulated steps each
First 60 use a heuristic
Next 240 use a greedy-eps policy
Then we use the optimal policy and run a simulated rollout 5x at each training point to produce the curve
Heuristic seeds, greedy-eps optimizes! Training is stable and generally sample efficient

## Slide 11: Results: Training (25%)
Notes: Let’s look more closely at the simulated rollouts. Here’s a plot of a = argmax(Q(s,a)) during the training period. Clearly failing

## Slide 12: Results: Training (50%)
Notes: 50% - now it’s minimizing the peaks and avoiding saturation

## Slide 13: Results: Training (75%)
Notes: 75% is driving it close to zero

## Slide 14: Results: Training (90%)
Notes: 90% sees stable peaks that are close to zero in both EW and NS phases

## Slide 15: Results: Head-to-Head Comparison
Conventional: NS for 10 sec → EW for 8 sec → NS…
Learned policy:
Notes: At 100% we compared it head-to-head. L is EW learned vs conventional. R is NS.
Reinforcement is doing a much better job of keeping the lengths down by effectively switching the light faster
Simulated 50 rollouts and the learned undiscounted reward was about 25% better than the conventional
Primary reason is that the RL system learned to reason over the states, while the conventional cannot see the states

## Slide 16: Results: Robustness
Use the trained Q(s, a) on a different model, where and are decreased 25% and and are increased 50%.
Notes: Let’s expand this idea by looking at how robust this is.
Using the same controllers we now perturb the traffic model by increasing the EW flows by 50% and decreasing the NS by 25% (to ensure a stable intersection)
Conventional analysis fails in EW while the RL controller kept the queues low
NS performed similarly
Numerical improvement too

## Slide 17: Conclusions and Future Work
Conclusions:
Signalized traffic system can be represented using an MDP formulation
A maximum likelihood RL to solve the MDP.
A learned model outperforms the state-of-the-art on a trained system and on a perturbed system.
Future Work:
POMDPs: exact queue lengths are required to solve the MDP, which may not be fully known. A POMDP formulation may better represent a physical system
Continuous state-space: this formulation is sensitive to state explosion under complex phasing. A continuous state-space may handle this better.
Notes: Read out

## Slide 18: Citations

## Slide 19: Appendix: Nominal Performance
Capacity and critical movement timing as applied to the model. Queue lengths are stable with time.

## Slide 20: Appendix: Perturbed Performance 1
Capacity and critical movement timing as applied to the model, but the NS phase is given an additional 2 time-intervals and EW is reduced by 2.

## Slide 21: Appendix: Perturbed Performance 2
Capacity and critical movement timing as applied to the model, but the NS incoming flow is increased by 50%.